Varian FDF to DICOM Conversion Utility
Software Design Document

Version 0.1
August 29, 2010

Prepared for
Varian, Inc. / Agilent Technologies
by
Stacy Maydew
DJSM Consulting, LLC

Revision History
Description	Revision	Date	Author
Original Version	0.1	08/29/10	Stacy Maydew / DJSM Consulgin, LLC

# Introduction
This document provides a high level description of the FDF to DICOM image conversion utility FdfToDcm.
The FdfToDcm utility is designed to convert MR and Spectroscopy images created by Varian equipment from their original, proprietary format, into standard DICOM 3 image sets. The output of the utility can be read by most standard DICOM display workstations and applications as well as being transmitted to a DICOM storage server.
In addition to creating the standard DICOM MR header tags, the user is given the ability to create custom DICOM tags that may be 1) part of the DICOM standard but the information is not contained in the raw data sets, or 2) vendor specific tags that are not part of the DICOM 3 standard.
Note: The FdfToDcm application does NOT provide the ability to send or receive images to or from DICOM storage servers.
# Program Usage
The following sections provide a basic overview of how the conversion application is used. The descriptions include general usage, detailed descriptions of the available options as well as a description of the method used to create custom DICOM tags.
## Basic Usage
The FdfToDcm application is written as a command line utility that can be invoked either directly via a terminal window, or it may be called as part of a shell script. The application will process all raw images in the directory location provided by the user or script and output a DICOM image for each input image.
In addition to processing the image data, the application reads information from the file “procpar” which should be located in the same directory as the input images.
## Program Options
There are three options available to the user when invoking the FdfToDcm application – '-if', '-of', and '-np'. The '-if' and '-of' options are mandatory and the '-np' is optional. Details of each option are given below.
- -if – This option must be present and must be the full path to the directory in which the input images reside
- -of – This option must be present on the command line and must point to the full path of the directory in which the user wishes the output DICOM images to be written. The output directory may be the same as the input directory.
- -np – This option indicates to the application that it should NOT include the contents of the procpar file in the output DICOM images. This option is not required. If not present, by default the application will insert the entire contents of the procpar file in a vendor specific DICOM tag.
## Custom DICOM Tags
In order for the user to add custom tags to the output DICOM files, the FdfToDcm application will search for a file named dicom.default. This file should contain tags defined by the user and those tags will be inserted by the application after all other processing has been completed.
The custom tag file contains text that describes individual DICOM tags the user wishes to add to the output images. The custom tags will be added to all images in the given data set.
### Custom Tag Syntax
Each tag in the custom tag file must adhere to the following format:
GGGG,EEEE	VR	<Tag Value>	# Optional comments
Where GGGG is the DICOM group (Hex) the tag belongs to, EEEE is the element (Hex) identifier, VR is the Value Representation of the tag, and the <Tag Value> is the data associated with the tag – in the format dictated by the value of VR.
(0008,0033) TM [125958.9876] # Content Time
The above example will insert the value 125958.9876 into the DICOM tag 0x0008,0x0033 which is called “Content Time”. In this case, the Value Representation is TM which indicates the <Tag Value> must represent a time value as described in Part 5 of the DICOM standard.
The possible VR values can be found in Part 5 of the DICOM standard. There is also a well written description of all VR types at the web site http://idlastro.gsfc.nasa.gov/idl_html_help/Value_Representations.html.
There are several types of tags that may be contained in the custom tag file, all of which MUST adhere to the DICOM standard in terms of the appropriate VR for a given tag.
Additionally, the text of the tags in this file must adhere to the following rules:
- Blank lines and lines that begin with the character '#' are considered comments and will be ignored
- Tags whose value begins with the character '=' are treated as pointers to the procpar file. The application will lookup the value in the procpar file and insert that value into the tag as defined by GGGG,EEEE and VR
- Tags whose value is enclosed in parentheses are considered unused and will be ignored
- Any tags whose group value GGGG is 0000, 0008 or 0028 will be ignored. These groups are filled in by the application and cannot be modified by the user.
- Tags which are represented by strings must have the <Tag Value> enclosed in square brackets – '[' and ']'.
Note: The Value Representations OB, OW and OF are not currently supported by the application.
### Custom Tag File Location
The application will attempt to locate the custom tag file by looking in several directories. In order to locate the custom tag file, the application will search the following directories, in the following order:
- The input directory specified by the '-if' option
- $HOME/vnmrsys/ (or ~/vnmrsys/)
- /vnmr/user_templates/plot
If the application is unable to locate a file named dicom.default in any of the above directories, it is assumed that there are no custom tags required for the current data set and the custom tag processing will not occur.
# Design Overview
The FdfToDcm application is written as a simple processing loop that will process each image in the user specified directory and create a DICOM output image for each input image. There are several options and external data sources that may be present that will also be processed on a per image basis. Those optional inputs include custom, user defined tags and inclusion of the procpar file as a user defined DICOM tag.
The following section gives a high level description of the program's logic flow and individual processing operations.
## Program Flow
The following diagram depicts the high level flow of the FdfToDcm application. More detailed descriptions of each individual processing operation can be found in subsequent sections.

Diagram 1: High Level Program Flow

## C++ Source Modules and Header Files
The FdfToDcm application consists of several individual C++ files source and header files. The following sections give brief descriptions of the each individual C++ modules, header files and their functionality and usage within the FdfToDcm application.
The following sections describe the individual source code modules that comprise the application. Where practical, the application is designed such that each source module serves a separate and distinctly different function than other source modules.
Although the application is compiled as a C++ program, the code is written primarily using basic C constructs as opposed to C++ classes. The exception to the previous statement is the interaction the application performs with the dicom3tools libraries. Interaction with the dicom3tools libraries is done using C++ classes.
### FdfToDcm.cpp
The FdfToDcm.cpp module contains the main() function of the FdfToDcm application. The main() function is basically a simple for() loop that performs all high level processing of each individual image or data set.
The basic sequence used within the main() function is as follows:
- Parse and validate all options
- Ensure that the input directory specified by the user exists
- For each file in the directory determine if it is an FDF or FID file
- Process the procpar file for the given study
- For FDF files:
  - Process the FDF header fields
  - Find the terminating null character in the FDF header and read in the pixel data that follows the null character
  - Normalize the pixel data to 16-bit and write them to a temporary file
- For FID files:
  - Process the FID data
- Create the DICOM objects that will be used to hold the header and pixel data
- Fill in common DICOM tags from the FDF header and the procpar file
- Calculate the positional information
- Process the custom tag file if it was specified by the user
- Insert the procpar file as a custom tag if the '-np' option was NOT specified
- Add the pixel data to the DICOM object and finalize the object
- Cleanup open files and any memory allocated on a per image basis
The above steps are basically the same as the program flow as described in the section 3.1. Program Flow.
The DICOM object is built dynamically using constructs defined in the dicom3tools libraries. The DICOM object is stored internally during processing in a ManagedAttributeList object. Individual tags are inserted using the ManagedAttributeList operator '+=' and the method defined for this operator and a given VR. For example, the StudyInstanceUID tag is a dot separated string of VR type UI and can be inserted using the following method:
- By Tag Name – The method call below will insert the string contained in the variable studyUID into the tag deifned by StudyInstanceUID:
  - list+=new UIStringAttribute(TagFromName(StudyInstanceUID), studyUID);
- By Tag Value – The method call below will insert the string in the variable valuestr into the DICOM tag defined by the variables group and element:
  - list+=new DecimalStringAttribute(Tag(group, element), valuestr);
NOTE: These two functions are crucial to understanding the FdfToDcm application for those who may be tasked with enhancing the application in the future.
### ProcessCustomTags.cpp
The ProcessCustomTags.cpp module contains the processing for the custom tags described in section 2.3. Custom DICOM Tags. The custom fields are processed using the following basic steps:
- Read the text line for a single tag
- Determine the data type for the field
- Isolate the VR and data value strings
- If the value is to be read from the procpar file, read that value
- Create the DICOM tag based on the group and element values and the specified VR
Note: If the string in the custom tag file does not strictly adhere to the formats described in section 2.3. Custom DICOM Tags, or the value portion of the input does not adhere to the VR for the specified DICOM tag, the behavior of the FdfToDcm application is undefined. In some cases, the tag will simply be ignored. In other cases, since the application cannot always determine the user's intentions from the limited information provided in a custom tag entry, the input may cause invalid tags to be inserted into the DICOM image, or may in rare cases cause the application to crash.
### ProcessFdfHeader.cpp
FDF files are formated with a text header at the beginning of the file, followed by the pixel data. The text header and the pixel data are separated by a single null byte.
The FDF header consists of a series of text lines written using C constructs. For example, the following string would define the sequence name assigned to the file:
char *sequence = "se3d";
The function ProcessFDFHeader() is called by the main() function and fields are processed using the following steps:
- Isolate the data type, name of the field and the field value from the input string
- Call ConvertFdfFieldToTag to populate the internal FDF header structure
As a result of this processing, no DICOM tags are created directly. Only the internal FDF header structure is filled in at this point. The main processing function will use the FDF information to create the appropriate tags.
### ConvertFdfFieldToTag.cpp
The file ConvertFdfFieldToTag.cpp is a simple file that basically contains a single function – convertFdfFieldToTag().
The function convertFdfFieldToTag() takes input from the initial FDF header processing as described above. Using the field name, data type and value as read from the input data file, this function basically consists of a large if/else statement that will find the field being processed based on the name of the field. Once found, it will convert and store the field value into the proper FDF header structure element.
Note: The name of this file/function may be a bit misleading in that no DICOM tags are actually created using the code in this module.
### ProcessFidData.cpp
The FID, or raw data is in a different format than that of the FDF image files. The FID data is described by file and block headers embedded in the raw data. The file header indicates the type of pixel data and the number of blocks of pixel data in a given defined in FidData.h.
The code in ProcessFidData.cpp will perform the following operations when processing a single image file.
- Read the file header
  - Determine the pixel type (short, int, or float)
  - Determine the number of blocks contained in the file
- For the number of blocks defined in the file header, perform the following operations:
  - Read the block header
  - Read the pixel data and note the pixel min andmaxvalues
  - Write the pixel data to a temporary file
- When all blocks have been processed, perform the following:
  - Normalize the data using the min and max pixel values
  - Write the pixel values to a temporary file which will be read during final processing in the main module FdfToDcm.cpp.
Note that there are no values contained in the FID data files that are placed into DICOM tags other than the pixel data itself. All tag values are read or calculated from information contained in the procpar file which is described in the following section 3.2.6. ProcessProcpar.cpp .
### ProcessProcpar.cpp
ProcessProcpar.cpp contains functions that specifically deal with parsing fields contained in the procpar file for a given set of data. For each line in the procpar file, the functions will perform the following actions:
- Read an entry
- Determine the data type – int, float, or string
- If the field is common to FDF files, place the field's value into an FdfHeader structure.
- If the field is used for computing positional information (FdfToDcm.cpp), save the values to the return variables
- If the above two processing steps do not find the field, process the field using a large “switch()” statement which directly inserts the field value(s) into the DICOM image header.
Note: Not all fields that may appear in a procpar file are recognized by the application. Fields that are not recognized during this processing are ignored. If required to be in the output images, these values may be placed in the custom tag file as described in section “2.3Custom DICOM Tags“.
### FdfHeader.h
The FdfHeader.h file contains structure definitions which describe all currently defined fields that may appear in an FDF image header. The file defines structures that define the name and data type of all FDF fields. These structures are referenced by ProcessFdfHeader.cpp, FdfToDcm.cpp and ConvertFdfFieldToTag.cpp.
### FidData.h
The header file FidData.h was taken directly from previous Varian applications. There were no changes to this file for the FdfToDcm application. Structures in this file are used when processing raw, FID image files. The structures are only used to calculate the size of the data set in pixels and to loop through the blocks of data that comprise an FID image.
### Procpar.h
The header file procpar.h contains only a single structure which defines the internal representation of a single procpar file entry. The entire contents of the file are included below.

#ifndef PROCPAR_H
#define PROCPAR_H

typedef struct procparEntry
{
int	type;
char	name[32];
;
float	fvalue;
};
typedef struct procparVals
{
procparEntry_t	date;

} procparVals_t;

#endif	// #ifndef PROCPAR_H

# Operating Environment
The following sections briefly describe the environment in which the FdfToDcm application is built and executed. These descriptions are very concise due to the fact that no non-standard tools or environmental setup is required for the FdfToDcm application.
## Build Environment
The application was developed using the Eclipse IDE (http://www.eclipse.org). The make files are automatically generated by Eclipse and are included with the FdfToDcm application distribution.
The application was developed on a 32-bit version of the Ubuntu Linux operating system. Source files are compiled using GNU C++ version 4.4.1 and GNU make version 3.81.
Although specific versions of the development tools is called out in this document, the application as well as the dicom3tools libraries should compile with any relatively recent version of Linux and the GNU tools mentioned above.
## Run Environment
Other than the library inclusions described in the section “5 External Dependencies“ below, there are no special runtime requirements for the FdfToDcm application.
# External Dependencies
There are very few external dependencies required by the FdfToDcm application beyond the normal libraries that are required by most C/C++ applications. Currently, the exception to this statement is the inclusion of libraries from the dicom3tools distribution. These libraries are described briefly in the following section.
## Dicom3tools Libraries
Creating DICOM headers and images is very much a non-trivial task. Due to the complexity of the requirements defined by the DICOM standard, creating a DICOM implementation from scratch is not a realistic option. Due to the widespread use of the standard in the medical field, many open source projects have been created to perform DICOM functions. The most widely used of these is the dicom3tools distribution created by David Clunie and maintained at http://www.dclunie.com.
The libraries should be compatible with most Linux platforms without recompiling. Exceptions will exist though, so if unsure, the libraries should be rebuilt if the application is moved to a different platform. This is true for a different distribution of Linux, but is particularly applicable for 32-bit vs. 64-bit platforms. The libraries MUST be recompiled if moved from a 32-bit machine to a 64-bit machine and vice versa.
To build the libraries, including associated man pages, execute the following from the directory in which the distribution was unpacked:

# ./Configure
# setenv IMAKEINCLUDE -I./config # only needed for Sun systems
# imake -I./config -DInstallInTopDir -DUseVarianID
# make World
# make install	# into ./bin
# make install.man	# into ./man

Executing these steps will place the output into the current working directory. The library output directory must be included in the paths defined by $LD_LIBRARY_PATH, or in another standard library location such as /usr/lib.
The make files included with the application assume that the libraries reside in the directory ../../dicom3tools. If the output directory is overridden, the make files must be changed to match.

– End Document –